## Slide 1: Applying Statistical Analysis on Geospatial Natural Hazard Raster Data
Jason Catelli
MGIS Candidate
GEOG 596A
Dr. Patrick Kennelly – Advisor
May 8, 2014

## Slide 2: Presentation Overview
Background
  General
  Data
  Project
  Statistics
What has been done?
Objective
Methodology
Timeline
Future Adaptations

## Slide 3: Background: General
2011 Lower Mississippi River Flooding
  Arkansas, Illinois, Kentucky, Louisiana, Mississippi, Missouri, and Tennessee
  21,000 homes and businesses impacted
  Damaged many levee systems
  ~ $3 Billion in damages
2011 Virginia Earthquake
  5.8 Magnitude
  Felt across the East Coast
  Largest east of the Rockies since 1897
2012 Superstorm Sandy
  Westward “Right-turn” path
  Lowest barometric pressure ever recorded for an Atlantic storm to make landfall north of Cape Hatteras, NC (940mb)
  Extreme storm surge
    13.88 feet at Battery Park in NYC
    32.5 foot wave measured by buoy in New York Harbor

## Slide 4: Background: General
Return periods or recurrence intervals
  The % chance of exceeding a certain threshold over 1 year
    100-yr flood event is a 1 in 100 chance or 1% chance over 1 year
    500-yr magnitude earthquake is a 1 in 500 chance or 0.2% chance over 1 year
    1000-yr storm surge flooding refers to 1 in 1000 chance or 0.1% chance over 1 year
  How are these numbers used?
    Insurance companies and public entities use return periods to understand the risk and prepare for catastrophic extremes
    Policies and pricing can be set based on the chance of events with respect to a geographic region
    Catastrophe models simulate events and can produce return periods based on historical and simulated results
    Protection structures are built to heights based on values of a particular return period

## Slide 5: Background: General
So how rare were these events?
  2011 Lower Mississippi River Flooding
    ~75-200-yr event (AIR Worldwide, 2011)
  2011 Virginia Earthquake
    1000-1300-yr event (Chapman, 2012)
  2012 Superstorm Sandy
    Westward “Right-turn” path (Hall, 2013)
      700-yr event
    Extreme storm surge (Sweet, 2013)
      ~300-yr Sandy Hook, NJ
      ~1500-yr The Battery, Lower Manhattan

## Slide 6: Background: Data
Natural hazard analysis is typically best implemented using gridded data
  Data is usually natively in a raster format
  Uniform point data can be easily converted to grid data
  Point data can be interpolated to a grid
  Many overlay functions are simple to perform using raster data
Utilizing Map Algebra
  Concept is very similar to mathematical algebra
  Operators and functions can be applied to grid values to produce new values (raster grids)
  Performed on individual or collection of rasters

## Slide 7: Background: Data
Types of raster analysis
  Local – works on a cell by cell basis
  Focal (neighborhood) – uses surrounding cells
  Zonal – uses defined zone input layer
  (Albrecht, 2007, p. 57)

## Slide 8: Background: Project
US Gulf and East Coast storm surge dataset development
  Goal of project to create two raster datasets representing 100-yr and 500-yr storm surge flood elevations
  Current process involves simulating thousands of synthetic storm surge events across the project area utilizing SLOSH (Sea, Lake, and Overland Surges from Hurricanes) model data
  Based on results derived from the SLOSH model, a series of interpolations were performed at both the SLOSH basin level as well as the event level
  Final result for each event consists of several rasters representing two iterations of interpolations along with their respective variance
  All results tied to a project-wide raster with unique cell IDs

## Slide 9: Background: Project
SLOSH Basin Coverage (NOAA)

## Slide 10: Background: Project
US Gulf and East Coast storm surge dataset development
  Goal of project to create two raster datasets representing 100-yr and 500-yr storm surge flood elevations
  Current process involves simulating thousands of synthetic storm surge events across the project area utilizing SLOSH (Sea, Lake, and Overland Surges from Hurricanes) model data
  Based on results derived from the SLOSH model, a series of interpolations were performed at both the SLOSH basin level as well as the event level
  Final result for each event consists of several rasters representing two iterations of interpolations along with their respective variance
  All results tied to a project-wide raster with unique cell IDs

## Slide 11: Background: Project
Interpolation at SLOSH Basin level

## Slide 12: Background: Project
Interpolation at Event level

## Slide 13: Background: Project
US Gulf and East Coast storm surge dataset development
  Goal of project to create two raster datasets representing 100-yr and 500-yr storm surge flood elevations
  Current process involves simulating thousands of synthetic storm surge events across the project area utilizing SLOSH (Sea, Lake, and Overland Surges from Hurricanes) model data
  Based on results derived from the SLOSH model, a series of interpolations were performed at both the SLOSH basin level as well as the event level
  Final result for each event consists of several rasters representing two iterations of interpolations along with their respective variance
  All results tied to a project-wide raster with unique cell IDs

## Slide 14: Background: Project
Project Grid

## Slide 15: Background: Project
US Gulf and East Coast storm surge dataset development (continued)
  Process written in Python and utilizes Arc Advanced, Spatial Analyst, and Geostatistical Analyst.
  Entire project to this point (with the exception of the SLOSH work) has been accomplished utilizing GIS
  Final code output places the results for each event into a text file with cell ID on global grid and corresponding values
  Current plan is for a colleague to create a code to read each event text file and for each project-wide grid cell determine each participating event for that cell and value
  Final goal to then apply extreme value theory to determine 100-yr and 500-yr values for each cell within global grid

## Slide 16: Background: Statistics
Extreme Value Theory
  “Techniques and models for describing the unusual rather than the usual” (Coles, 2001, p. vii)
  Goal of EVT to quantify stochastic or random behavior of processes or phenomena at a very large or very small scale
  Involves predicting extreme values beyond what has already been observed
  Levee example – determine the height to build to for 500-yr protection

## Slide 17: Background: Statistics
Extreme Value Theory - Block Maxima/Minima Technique
  Divide data into equal sized time intervals/blocks (i.e. by month)
  Determine the maximum value for each block
  Estimate Generalized Extreme Value (GEV) distribution fitted to block maxima
  Calculate return value function and uncertainty
https://www.isse.ucar.edu/extremevalues/back.html

## Slide 18: Background: Statistics
Extreme Value Theory - Peak Over Threshold Technique
  Select a threshold
  Extract exceedances from data
  Fit exceedances to General Pareto (GP) Distribution (conditional distribution)
  Estimate unconditional distribution and return values
https://www.isse.ucar.edu/extremevalues/back.html

## Slide 19: What has already been done?
Risk Assessment of Hurricane Storm Surge for New York City (Lin et al., 2010)
  Simulated large number of synthetic hurricane events
  Storm surge values based on SLOSH model data
  Used peaks-over-threshold method with the generalized Pareto distribution to generate return periods

## Slide 20: What has already been done?
Drought Risk Assessment (Tonini, 2013)
  Used extreme value analysis to calculate maximum monthly temperatures contributing to drought conditions
  GIS-based analysis
  Custom Python script and toolbox created utilizing calls to R statistical package
  Block maxima technique only

## Slide 21: Objective
To apply statistical analysis to geospatial raster data to calculate values for desired return periods on natural hazard data.
How will this be achieved?
  Explore existing methodologies to determine which (if any) techniques would fit current project
  Formulate a series of methods to perform statistical analysis on geospatial raster data in an advanced statistical package utilizing the Python programming language.

## Slide 22: Methodology
Evaluate current code
Move rasters to array structures utilizing SciPy’s NumPy library
Evaluate functions offered by SciPy
Evaluate functions offered by outside statistical packages as pertains to extreme value theory
Develop new code to connect array structure to statistics offered by SciPy and/or through an outside statistical package
Produce sample output and compare to results derived by colleague’s process

## Slide 23: Methodology
SciPy - www.scipy.org
  Python-based open-source software for mathematics, science, and engineering
  NumPy library – fundamental library for numerical computing
    Numerical (multi-dimensional) arrays and matrix types
    Key piece to the project – moving raster data out of ArcGIS into this format for optimized processing
    RasterToNumPyArray / NumPyArrayToRaster
  SciPy.stats
    Large number of probability distributions
    Library of statistical functions

## Slide 24: Methodology
Evaluate current code
Move rasters to array structures utilizing SciPy’s NumPy library
Evaluate functions offered by SciPy
Evaluate functions offered by outside statistical packages as pertains to extreme value theory
Develop new code to connect array structure to statistics offered by SciPy and/or through an outside statistical package
Produce sample output and compare to results derived by colleague’s process

## Slide 25: Methodology
R - http://www.r-project.org/
  Free software environment for statistical computing and graphics
  Wide variety of statistical and graphical techniques
  Highly extensible
  Contains suite of operators to perform calculations on arrays and matrices
  Large collection of intermediate tools for data analysis
  Well developed, simple, programming language

## Slide 26: Methodology
Evaluate current code
Move rasters to array structures utilizing SciPy’s NumPy library
Evaluate functions offered by SciPy
Evaluate functions offered by outside statistical packages as pertains to extreme value theory
Develop new code to connect array structure to statistics offered by SciPy and/or through an outside statistical package
Produce sample output and compare to results derived by colleague’s process

## Slide 27: Timeline
Summer 2014
  Research
    Evaluate current code
    Investigate SciPy and utilization of NumPy arrays
    Investigate outside statistical packages
    Determine connection between Python and statistical packages
  Code Changes
Fall 2014
  Code improvements
  Complete report
Late Fall 2014/ Spring 2015
  American Geophysical Union Conference?
  American Association of Geographers Conference?

## Slide 28: Future Adaptations
Utilizing Extreme Value Theory for other hazards
  Flood modeling
  Wind events
  Earthquakes
Additional statistical analysis beyond Extreme Value Theory
  Ability to move from ArcGIS to outside statistical package
  Utilization of SciPy to improve code performance by tapping into multi-dimensional arrays

## Slide 29: Acknowledgements
Dr. Patrick Kennelly - Advisor
Dr. Shangyao Nong - Colleague

## Slide 30: Sources
AIR Worldwide. “Alert Worldwide: Mississippi River Flooding.” Last modified May 13, 2011. http://alert.air-worldwide.com/EventSummary.aspx?e=554&tp=54&c=1.
Albrecht, Jochen. Key Concepts and Techniques in GIS. London: SAGE Publications Ltd., 2007.
Chang, Kang-Tsung. Introduction to Geographic Information Systems. Texas: McGraw-Hill, 2003.
Coles, Stuart. An Introduction to Statistical Modeling of Extreme Values. London: Springer-Verlag, 2001.
Chapman, Martin. “The August 23, 2011 Earthquake in the Central Virginia Seismic Zone.” Presentation at the USGS National Seismic Hazard Mapping Workshop, Memphis, Tennessee, February 22-23, 2012.
Hall, T. M., and A. H. Sobel. “On the impact angle of Hurricane Sandy's New Jersey landfall” Geophysical Research Letters. May 28, 2013: 2312–2315.
Lin, N., K. A. Emauel, J. A. Smith, and E. Vanmarcke. “Risk Assessement of Hurricance Storm Surge for New York City.” Journal of Geophysical Research. September 25, 2010.
Nong, Shangyao, Jeffrey McCollum, Liming Xu, Michael Scheffler, and Hosam Ali. “Probabilistic Storm Surge Heights for the US Using Full Stochastic Events.” Paper presented at the AMS 29th Conference on Hurricanes and Tropical Meteorology, Tucson, Arizona, May 10-14, 2010.
O’Sullivan, David, and David J. Unwin. Geographic Information Analysis. New York: Wiley, 2010.
Sweet, William, Chris Zervas, Stephen Gill and Joseph Park. “Hurricane Sandy Inundation Probabilities Today and Tomorrow.” Bulletin of the American Meteorological Society. September 2013: 517-20.
Tonini, Francesco. “Drought Risk Assessment – A Customized Toolbox.” Presentation at the ESRI International User Conference, San Diego, California, July 8-12, 2013.
Walton, Todd L. “Distributions for Storm Surge Extremes.” Ocean Engineering. December 2000: 1279-1293.