## Slide 1: Assuring Connectivity in an Electric Utility GIS Distribution Model
Matthew D. Coram, GIS Analyst
Murfreesboro Electric Dept., TN
Advisor: Dr. Amy Griffin
July 28, 2016

## Slide 2
Timeline
Work began: Spring 2016
Class and presentation: July 28, 2016
Presentation: ESRI’s GeoConX conference during the week of October 2016 in Phoenix, AZ
Project Completion: Early Spring 2017

## Slide 3
About MED and the GIS Department
Murfreesboro is 30 minutes southeast of Nashville
Municipal Electric Utility with approximately 58,000 electric meters
GIS Department is a subset of IT and supports every other department
Weekly workflows include importing of developer CAD files and conversion of constructed electric lines into master database

## Slide 4
Spans and Edges
ESRI’s Geometric Network Model - Edges
  Simple Edge – Line where all of the flow entering is equal to all of the flow leaving
  Complex Edges – Line where all of the flow may be split among the end and laterals
  Complex edge may be thought of as multiple simple edges

## Slide 5
Spans and Edges
MED uses simple edges exclusively
Junctions (point features) present at all span endpoints
A simple edge may be split into two simple edges when a new tap is constructed

## Slide 6
Spans and Edges
Example of Simple Edge
Valve
102
Junction
1630

## Slide 7
Spans and Edges
Example of Complex Edge
Valve
102
Junction
1630
Junction
1842

## Slide 8
Background
Traditional GIS used an attribute-based numbering system for electrical lines
Newer systems have moved toward a GUID-based approach
Database tables are designed to be normalized and to help prevent unwanted data changes
Meaning of electrical spans

## Slide 9
Conversion
Legacy GIS used non-intersecting spans
ESRI-based system requires spans to be snapped together
Connectivity is our focus
Other systems rely on GIS data, so accuracy is key

## Slide 10
Connectivity
Every piece of equipment and all lines on a circuit are interconnected
Some coincident features may not have connectivity – Double Circuits

## Slide 11
Connectivity
Relationships, endpoints, and insertion points are important
Feature dataset table with a related stand-alone table
Two sources must be in agreement for connectivity to work properly

## Slide 12
Dilemma
Many instances of disagreement between two data sources
These issues can interrupt connectivity
Difficult to detect until each instance is found through editing
Span endpoints may be inches or feet apart

## Slide 13
Application Operation
Begins at the substation (source)
Steps through each junction and span
Junctions with multiple downstream spans must be remembered
At the end of each branch, program begins on next unprocessed branch
Program continues until each branch has been checked, then starts on next circuit

## Slide 14
Application Operation - Example
Span endpoints are not snapped to one another

## Slide 15
Application Operation - Example
all_relationships table indicates no issues with the connectivity

## Slide 16
Application Operation - Example
Likely that some or all of the downstream features will be disconnected
In the OMS, customers may be out of power but may not be reported correctly
Customer relations may be impacted

## Slide 17
Custom Application
Custom solution is needed to identify issues
Primary and Secondary network issues may potentially be identified
Dealing with a third-party provider, so a data export is needed
Exported data will be operated upon and return a separate feature dataset for import to GIS
Overlay Analysis allows new dataset to highlight problem areas

## Slide 18
Network Types
Primary – Higher Voltages
Secondary – Lower Voltages
Transformer is the dividing line between the two network types
Primary and Secondary network issues may potentially be identified by the application

## Slide 19
Network Types
Primary – Red Lines
Secondary – Orange Lines
Transformers – Red Triangles
Meters – Green Symbols

## Slide 20
Custom Application
Use of vendor-supplied tools to correct broken connectivity
New dataset to have attribute for tracking when corrections have taken place

## Slide 21
Custom Application
Entity Relationship Diagram (ERD)
Relates the all_spans feature dataset to the all_relationships connectivity table

## Slide 22
Application – Return on Investment
Errors of this type cannot be automatically detected without the application
Estimates
  Manual correction (after research) can take between 5 and 10 minutes
  Number of system-wide errors may range from 500 to 1,000

## Slide 23
Application – Return on Investment
Research per Primary spans
  ((0.5 min * 22,500 spans) / 60 min per hour) = 187.5 working man-hours
Error Repair for Primary spans
  ((10 min * 1,000 errors) / 60 min per hour) = 166.67 working man-hours
Total of 354.17 man-hours or approximately 8.8 man-weeks (10 – 12 weeks more realistic?)
Secondary networks more numerous, longer time

## Slide 24
Application – What’s down the road?
Conversion from Microsoft Access’ Visual Basic for Applications (VBA)
C# (.NET) is likely the preferred language
Possible move from storage of data in MS Access to MS SQL Server
Improved tracking in program development
Increased execution speed
Ability to interact with the map document

## Slide 25
Application Goals
Detect issues with connectivity
Mark those errors for manual correction
Facilitate correction and minimal tracking for editor convenience
Increase confidence in the OMS
Increase confidence in the Engineering Model to accurately predict growth

## Slide 26
Questions?

## Slide 27
Sources
Environmental Systems Research Institute, Inc. (n.d.). ArcGIS Help. Retrieved July 27, 2016, from http://desktop.arcgis.com/en/arcmap/10.3/manage-data/geodatabases/design-an-overview-of-table-properties.htm
Environmental Systems Research Institute, Inc. (n.d.). ArcGIS Help. Retrieved June 30, 2016, from http://desktop.arcgis.com/en/arcmap/10.3/manage-data/geodatabases/exercise-5-building-a-geometric-network.htm
Environmental Systems Research Institute, Inc. (n.d.). ArcMap. Retrieved June 30, 2016, from http://desktop.arcgis.com/en/arcmap/latest/manage-data/geometric-networks/about-creating-geometric-networks.htm
Environmental Systems Research Institute, Inc. (n.d.). ArcMap. Retrieved June 30, 2016, from http://desktop.arcgis.com/en/arcmap/latest/manage-data/geometric-networks/what-are-geometric-networks-.htm
Environmental Systems Research Institute, Inc. (n.d.). ArcMap. Retrieved June 30, 2016, from http://desktop.arcgis.com/en/arcmap/latest/manage-data/geometric-networks/a-quick-tour-of-geometric-networks.htm
ESRI 2011. ArcGIS Desktop: Release 10.2.2. Redlands, CA: Environmental Systems Research Institute.

## Slide 28
Sources
Gilgrass, C., & Hoel, E. (2012, July 26). Geometric Networks: An Introduction. Retrieved June 30, 2016, from http://video.esri.com/watch/2012/geometric-networks-an-introduction
Microsoft, Inc. (2010). Microsoft Access: Release 2010. Redmond, WA: Microsoft, Inc.
Murfreesboro Electric Department. (2016). MEDGIS01 [SQL Server Database]. Murfreesboro, TN: Murfreesboro Electric Department.
Rahm, E., & Do, H. (2000). Data cleaning: Problems and current approaches. IEEE Data Eng. Bull., 23(4), 3–13. http://doi.org/10.1145/1317331.1317341
O’Sullivan, D. (2014). GEOG 586 - Geographic Information Analysis. The Pennsylvania State University. Retrieved April 5, 2016 from https://www.e-education.psu.edu/geog586spring2/