## Slide 1: Statistical Analysis for Automated Seep Extraction in GIS
Presented by Pamela Kanu, GISP
Pennsylvania state university
Geog 596A Spring II 2017
MaY 11, 2017
Notes: Conduct literature review (narrative identifying significant literature, including identification of major issues discussed, approach used, lessons learned, history of issues, and future of the issues, include formal reference citations)

## Slide 2: Seeps
Seeps are natural gas and crude oil that enter the ocean through cracks and sediments along the seafloor. Seeps emit continuously into the ocean (similar to an oil spill and drift with currents)
Due to the warm environment caused by geologic activity, the escaping methane gas produce bacteria that benthos consume [1]
Oil slick on the sea surface
Estimated 160,000 tons of natural petroleum enter North American waters each year [4]
Tubeworm bush[4]
Notes: http://oceanexplorer.noaa.gov/explorations/02arctic/background/benthos/benthos.html
Animals that live on the seafloor are called benthos. Benthic communities are invertebrates, including sea anemones, sponges, corals, sea stars, sea urchins, worms, bivalves, crabs, etc.

## Slide 3: STUDY AREA
Vessel: Fugro Discovery
Instrument: Kongsberg EM302
  Seabed mapping with high resolution to depth of 7,000+ m [8]
Missing Malaysian Flight MH370 Survey offshore Australia from October 23, 2014 to August 11, 2016
Southern Indian Ocean, Offshore Australia
Image courtesy of Fugro
Broken Ridge
Water Column
Search Area

## Slide 4: Data acquisition
Data are acquired by sonar beams in a straight line swath width that captures meters of the surveyed area using GPS horizontal positioning and local water-level datums for vertical positioning
Accurate and precise horizontal and vertical positioning of the vessel are required to obtain an accurate sample of the water depth, water column, and seafloor
4 dimensions (XYZ and Time) are used to calculate and correct sounding locations [5]
Image courtesy of Fugro
Notes: “The amount of time it takes for the sound waves to bounce off the seabed and return to a receiver is used to determine water depth”

## Slide 5: Multibeam echosounder sonar data
Multi-Beam Echo Sounder
  Sonar that emit sound waves in a fan shape beneath the ship’s hull.
  Multibeam uses spatial filtering (beamforming), a signal processing technique for directional signal transmission where sound waves ping the seabed and reflect off to calculate the water depth
XYZ that is converted into a continuous raster
Multibeam (left) and Sidescan sonar (right) data acquisition.
Image courtesy of NOAA.
Notes: “The amount of time it takes for the sound waves to bounce off the seabed and return to a receiver is used to determine water depth”

## Slide 6: Water column data
Captured with acoustic beams from multibeam sonars
Used to map marine life, oceanic processes, and seeps[3]
XYZ points in the water column

## Slide 7: Existing seep extraction techniques
Manual Extractions
  2D and 3D for ArcGIS
  Visualizing in Fledermaus
Fledermaus FMMidWater
  Rapidly view and extract water column features from a range of sonar file by converting data into a Generic Water Column format (GWC) to use for further processing and visualization by threshold filtering[2]
Research algorithms University of New Hampshire Center for Coastal and Ocean Mapping Joint Hydrographic Center (UNH CCOM-JHC)
  Despeckle filter
  Feature detection tool
Qimera Midwater
  Add-on packages for water column processing
  Extended FMMidWater Tool used to reduce sonar noise and converting the water column data sample into bathymetric format [6]
Notes:   Despeckle filter – removes small defects and reduces noise
  Four steps for manipulating water column data:
    Import sonar file(s)
    Convert to GWC format
    Identify features of interest using threshold filtering
    Export to Fledermaus for visualization or ASCII for custom processing [11].

## Slide 8: Lessons Learned
Digitizing in 2D, lack of 3D visualizations in ArcGIS
Need for an extension to ArcGIS environment
Need for improving water column data processes due to large amounts of data and noise
No web component
Notes: This large volume of data must be recorded and protected from loss in some logical management scheme. The scheme must provide high performance access to facilitate efficient processing and visualization of such large amounts of data.

## Slide 9: Capstone objective
My Capstone Project is to map the gas bubbles (plumes) that seep from the seafloor for potential exploration site investigation
Define level of accuracy in seep extraction

## Slide 10: Methodology overview
Convert XYZ to Points
Calculate Density, Determine Threshold and Conversions
Extract Z Values
Calculate Water Column Height
Add Fields for Weights
Apply Statistical Algorithms
Remove Noise
DEM
Data Processing
TXT
Density
Weight Criteria
Spatial Statistics
Extract Seeps

## Slide 11: What ARE THE CHARACTERISTICS OF a seep?
Closer to the Seafloor (but not always the case)
Linear
Condensed
Related to Benthic Communities
Disparate Amplitude Intensity
Weight Criteria
Spatial Statistics
Extract Seeps

## Slide 12: Closer to the Seafloor (but not always the case)
Closer to the seafloor (but not always the case)
  Calculate water column heights
  Use a threshold of less than ~4 meters in the water column
Closer to the Seafloor (but not always the case)
Linear
Condensed
Related to Benthic Communities
Disparate Amplitude Intensity

## Slide 13: Linear
Seeps will appear in a linear fashion
  Bubbles locations are selected using Near_3D tool
  Follow Tobler’s Law, items that are closer are more related than items that are distant
Closer to the Seafloor (but not always the case)
Linear
Condensed
Related to Benthic Communities
Disparate Amplitude Intensity

## Slide 14: condensed
Seeps are in dense
  XYZ points are used to calculate density
  Seeps will be dense in the z value
  May be dense relative to the seafloor
Closer to the Seafloor (but not always the case)
Linear
Condensed
Related to Benthic Communities
Disparate Amplitude Intensity

## Slide 15: Related to benthic communities
Warm areas produce bacteria benthos consume
  Geology activity
  Analysis does not account for benthic communities
Closer to the Seafloor (but not always the case)
Linear
Condensed
Related to Benthic Communities
Disparate Amplitude Intensity
Tubeworm bush[4]
Notes: Identifying seeps could help identify or predict communities. Conversely, mapping communities can help identify seeps.

## Slide 16: Disparate Amplitude Intensity
Amplitude values will vary, but depending on the item will reflect similar intensities
  Items in the water column will reflect varying intensities
  Amplitude values are relative
Closer to the Seafloor (but not always the case)
Linear
Condensed
Related to Benthic Communities
Disparate Amplitude Intensity
Notes: These are the fields from the TXT files that are used to apply the criteria to the analysis.

## Slide 17: criteria
Bathy (Z)
Delta (Z)
Criteria
Weighted Description
Weighted Class
Fields | Value Description
Bathy (Z) | Depth of Seafloor
Delta (Z) | Depth between Feature and Seafloor
Criteria | Criteria Description
Weighted Class | Threshold
Weighted Description | Description of Weighted Criteria
Weight Criteria
Spatial Statistics
Extract Seeps

## Slide 18: Spatial statistics
Hot Spot Analysis tool to detect concentrations of high or low values [7]
Positive z-scores identify seeps
  The more intense the clustering of high values
Significantly negative z-scores identify fish
  The more intense clustering of low values
P-value
  Helps to determine the significance of the results [9]

## Slide 19: Accuracy Assessment
Select random points using Create Accuracy Assessment Points tool
Experts in seep industry will interpret random points
Compute Confusion Matrix table
Errors of Omission – Analysis may result in items being classified as seeps or bubbles within a seep, may be classified as not a seep.
Errors of Commission – User’s error as interpreted data is subjective [10]
Notes: Producer’s accuracy (Errors of Omission)

## Slide 20: Automated techniques
Python
Calculate Density, Determine Threshold and Conversions
Extract Z Values
Calculate Water Column Height
Add Fields for Weights
Apply Statistical Algorithms
Remove Noise
JavaScript
Customized Web Application for Viewing Extracted Seeps in 2D and 3D
Convert XYZ to Points

## Slide 21: Anticipated results AND DELIVERABLES
Accuracy Assessment
Perform an accuracy assessment using ArcGIS accuracy assessment tools
Account for errors of omission
Account for errors of commission
Seep Extraction
Feature class of extracted seeps
  Attributed tables from FMMidwater
Custom web application in ArcGIS for JavaScript
Automated seep detection process

## Slide 22: Timeline per week
Data Processing
Refine Analysis
Write Analysis Script
Data Migration
Web Application
Test Application
Deploy
Moving forward timeline:

## Slide 23: references
[1] Carrie C. Wall, J. Michael Jech, Susan J. McLean; Increasing the accessibility of acoustic data through global access and imagery. ICES J Mar Sci 2016; 73 (8): 2093-2103. doi: 10.1093/icesjms/fsw014
[2] QPS B.V. (2016, October 18). Fledermaus 7.7.x Manual. SAAB.
[3] http://www.whoi.edu/oil/natural-oil-seeps
[4] http://response.restoration.noaa.gov/oil-and-chemical-spills/oil-spills/resources/what-are-natural-oil-seeps.html
[5] https://www.nauticalcharts.noaa.gov/csdl/publications/TM_NOS-CS03_FY2003-Brown_SonarDataSystem.pdf
[6] http://www.qps.nl/display/qimera/Qimera_Midwater
[7] O’Sullivan, D., & Unwin, D. (2010). Geographic Information Analysis. Hoboken, New Jersey: 2nd John Wiley and Sons
[8] https://www.km.kongsberg.com/ks/web/nokbg0397.nsf/
AllWeb/A915A71E90B6CFAEC12571B1003FE84D/$file/306106_em_302_product_specification.pdf?OpenElement
[9] http://resources.esri.com/help/9.3/arcgisengine/java/gp_toolref/spatial_statistics_tools/how_hot_spot
_analysis_colon_getis_ord_gi_star_spatial_statistics_works.htm
[10] http://desktop.arcgis.com/en/arcmap/latest/manage-data/raster-and-images/accuracy-assessment-for-image-classification.htm