## Slide 1: Statistical Analysis for Automated Seep Extraction in GIS
Presented by Pamela Kanu, GISP
Underwater acoustic conference
& exhibition series
September 2017

## Slide 2
OUTLINE
DATA
SEEPS
STUDY
AREA
SONAR
DATA
RESULTS
ANALYSIS

## Slide 3: Seeps
Seeps are natural gas and crude oil that enter the ocean through cracks and sediments along the seafloor. Seeps emit continuously into the ocean (similar to an oil spill and drift with currents)
Due to the warm environment caused by geologic activity, the escaping methane gas produce bacteria that benthos consume [1]
Oil slick on the sea surface
Estimated 160,000 tons of natural petroleum enter North American waters each year [4]
Tubeworm bush[4]
Notes: http://oceanexplorer.noaa.gov/explorations/02arctic/background/benthos/benthos.html
Animals that live on the seafloor are called benthos. Benthic communities are invertebrates, including sea anemones, sponges, corals, sea stars, sea urchins, worms, bivalves, crabs, etc.

## Slide 4: STUDY AREA
Vessel: Fugro Discovery
Instrument: Kongsberg EM302
  Seabed mapping with high resolution to depth of 7,000+ m [8]
Missing Malaysian Flight MH370 Survey offshore Australia from October 23, 2014 to August 11, 2016
Southern Indian Ocean, Offshore Australia
Image courtesy of Fugro
Broken Ridge
Water Column
Search Area

## Slide 5: Data acquisition
Data are acquired by sonar beams in a straight line swath width that captures meters of the surveyed area using GPS horizontal positioning and local water-level datums for vertical positioning
Accurate and precise horizontal and vertical positioning of the vessel are required to obtain an accurate sample of the water depth, water column, and seafloor
4 dimensions (XYZ and Time) are used to calculate and correct sounding locations [5]
Image courtesy of Fugro
Notes: “The amount of time it takes for the sound waves to bounce off the seabed and return to a receiver is used to determine water depth”

## Slide 6: Multibeam echosounder sonar data
Multi-Beam Echo Sounder
  Sonar that emit sound waves in a fan shape beneath the ship’s hull.
  Multibeam uses spatial filtering (beamforming), a signal processing technique for directional signal transmission where sound waves ping the seabed and reflect off to calculate the water depth
XYZ that is converted into a continuous raster
Multibeam (left) and Sidescan sonar (right) data acquisition.
Image courtesy of NOAA.
Notes: “The amount of time it takes for the sound waves to bounce off the seabed and return to a receiver is used to determine water depth”

## Slide 7: Water column data
Captured with acoustic beams from multibeam sonars
Used to map marine life, oceanic processes, and seeps[3]
XYZ points in the water column

## Slide 8: Existing seep extraction techniques
Manual Extractions
  2D and 3D for ArcGIS
  Visualizing in Fledermaus
Fledermaus FMMidWater
  Rapidly view and extract water column features from a range of sonar file by converting data into a Generic Water Column format (GWC) to use for further processing and visualization by threshold filtering[2]
Research algorithms University of New Hampshire Center for Coastal and Ocean Mapping Joint Hydrographic Center (UNH CCOM-JHC)
  Despeckle filter
  Feature detection tool
Qimera Midwater
  Add-on packages for water column processing
  Extended FMMidWater Tool used to reduce sonar noise and converting the water column data sample into bathymetric format [6]
Notes:   Despeckle filter – removes small defects and reduces noise
  Four steps for manipulating water column data:
    Import sonar file(s)
    Convert to GWC format
    Identify features of interest using threshold filtering
    Export to Fledermaus for visualization or ASCII for custom processing [11].

## Slide 9: Need for additional analysis
Digitizing in 2D, lack of 3D visualizations in ArcGIS
Need for an extension to ArcGIS environment
Need for improving water column data processes due to large amounts of data and noise
No web component
Notes: This large volume of data must be recorded and protected from loss in some logical management scheme. The scheme must provide high performance access to facilitate efficient processing and visualization of such large amounts of data.

## Slide 10: objective
To map the gas bubbles (plumes) that seep from the seafloor for potential exploration site investigation
Define level of accuracy in seep extraction

## Slide 11: Methodology overview
Convert XYZ to Points
Calculate Density, Determine Threshold and Conversions
Extract Z Values
Calculate Water Column Height
Add Fields for Weights
Apply Statistical Algorithms
Remove Noise
DEM
Data Processing
TXT
Density
Weight Criteria
Spatial Statistics
Extract Seeps

## Slide 12: What ARE THE CHARACTERISTICS OF a seep?
Closer to the Seafloor (but not always the case)
Linear
Condensed
Related to Benthic Communities
Disparate Amplitude Intensity
Weight Criteria
Spatial Statistics
Extract Seeps

## Slide 13: Closer to the Seafloor (but not always the case)
Closer to the seafloor (but not always the case)
  Calculate water column heights
  Use a threshold of less than ~4 meters in the water column
Closer to the Seafloor (but not always the case)
Linear
Condensed
Related to Benthic Communities
Disparate Amplitude Intensity

## Slide 14: Linear
Seeps appear in a linear fashion
  Bubbles locations are selected using Near_3D tool
  Follow Tobler’s Law, items that are closer are more related than items that are distant
Closer to the Seafloor (but not always the case)
Linear
Condensed
Related to Benthic Communities
Disparate Amplitude Intensity
Notes: Move from seafloor to sea surface
Drift with the currents

## Slide 15: condensed
Seeps are in dense
  XYZ points are used to calculate density
  Seeps are dense in the z value
  May be dense relative to the seafloor
Closer to the Seafloor (but not always the case)
Linear
Condensed
Related to Benthic Communities
Disparate Amplitude Intensity

## Slide 16: Related to benthic communities
Warm areas produce bacteria benthos consume
  Geology activity
  Analysis does not account for benthic communities
Closer to the Seafloor (but not always the case)
Linear
Condensed
Related to Benthic Communities
Disparate Amplitude Intensity
Tubeworm bush[4]
Notes: Identifying seeps could help identify or predict communities. Conversely, mapping communities can help identify seeps.

## Slide 17: Disparate Amplitude Intensity
Amplitude values vary, but depending on the item, they may reflect similar intensities
  Items in the water column reflect varying intensities
  Amplitude values are relative
Closer to the Seafloor (but not always the case)
Linear
Condensed
Related to Benthic Communities
Disparate Amplitude Intensity
Notes: These are the fields from the TXT files that are used to apply the criteria to the analysis.

## Slide 18: criteria
Bathy (Z)
Delta (Z)
Criteria
Weighted Description
Weighted Class
Fields | Value Description
Bathy (Z) | Depth of Seafloor
Delta (Z) | Depth between Feature and Seafloor
Criteria | Criteria Description
Weighted Class | Threshold
Weighted Description | Description of Weighted Criteria
Weight Criteria
Spatial Statistics
Extract Seeps

## Slide 19: Spatial statistics
Hot Spot Analysis tool to detect concentrations of high or low values [7]
Positive z-scores identify seeps
  The more intense the clustering of high values
Significantly negative z-scores identify fish
  The more intense clustering of low values
P-value
  Helps to determine the significance of the results [9]

## Slide 20: Automated techniques
Python
Calculate Density, Determine Threshold and Conversions
Extract Z Values
Calculate Water Column Height
Add Fields for Weights
Apply Statistical Algorithms
Remove Noise
JavaScript
Customized Web Application for Viewing Extracted Seeps in 2D and 3D
Convert XYZ to Points

## Slide 21: results
Seep Extraction
Feature class of extracted seeps
  Attributed tables from FMMidwater
Custom web application in ArcGIS for JavaScript
Automated seep detection process

## Slide 22: results

## Slide 23: Results

## Slide 24: ARCgiS JAVASCRIPT 4.2
Custom API to handle data
Features hosted in ArcGIS, looking into opened sourced options - GeoServer
Web Server – Azure, Amazon, locally

## Slide 25: Accuracy Assessment
Select 100 random points for sample size
Errors of Commission – Analysis may result in items being classified as seeps or bubbles within a seep, may be classified as not a seep.
Producer’s Accuracy is Subjective – User’s error as interpreted data is subjective [10]
Notes: Producer’s accuracy (Errors of Omission)

## Slide 26: Accuracy assessment
100 random points manually identified each point on a Seep/Not a Seep basis.
Errors of commission were manually corrected
CLASSIFICATION | Total Random | No. Correct | Percentage Correct
NOT A SEEP | 58.00 | 57.00 | 98.28
SEEP | 42.00 | 34.00 | 80.95
 | 100.00 | 91.00 | 
Overall Accuracy 91%
Notes: Commissions were items that were misclassified

## Slide 27: Plans for the future
Continuously refining analysis to reduce noise
Develop an ArcGIS Add-In or open sourced software
Build functionality into web application
Multithreading / Further development for processing large datasets

## Slide 28
SUMMARY
Accuracy
Automated
Extension into ArcGIS
Seep
Hunting
Extension into Web
Questions?

## Slide 29: references
[1] Carrie C. Wall, J. Michael Jech, Susan J. McLean; Increasing the accessibility of acoustic data through global access and imagery. ICES J Mar Sci 2016; 73 (8): 2093-2103. doi: 10.1093/icesjms/fsw014
[2] QPS B.V. (2016, October 18). Fledermaus 7.7.x Manual. SAAB.
[3] http://www.whoi.edu/oil/natural-oil-seeps
[4] http://response.restoration.noaa.gov/oil-and-chemical-spills/oil-spills/resources/what-are-natural-oil-seeps.html
[5] https://www.nauticalcharts.noaa.gov/csdl/publications/TM_NOS-CS03_FY2003-Brown_SonarDataSystem.pdf
[6] http://www.qps.nl/display/qimera/Qimera_Midwater
[7] O’Sullivan, D., & Unwin, D. (2010). Geographic Information Analysis. Hoboken, New Jersey: 2nd John Wiley and Sons
[8] https://www.km.kongsberg.com/ks/web/nokbg0397.nsf/
AllWeb/A915A71E90B6CFAEC12571B1003FE84D/$file/306106_em_302_product_specification.pdf?OpenElement
[9] http://resources.esri.com/help/9.3/arcgisengine/java/gp_toolref/spatial_statistics_tools/how_hot_spot
_analysis_colon_getis_ord_gi_star_spatial_statistics_works.htm
[10] http://desktop.arcgis.com/en/arcmap/latest/manage-data/raster-and-images/accuracy-assessment-for-image-classification.htm