## Slide 1: Conveying Coastal Inundation Potential Associated with Extratropical (ET) Cyclones
Adrienne Leptich
National Weather Service / Penn State University
Esri International User Conference
July 11, 2017

## Slide 2: Overview
Background
Methodology
Results
Future Work
Tuckerton, N.J., inundated on Oct. 30 by the storm surge from Superstorm Sandy. Photo: U.S. Coast Guard

## Slide 3: Background

## Slide 4
Tropical Cyclones
  Energy from latent heat release
  No frontal features
  “Warm Core”
Extratropical Cyclones
  Energy from horizontal temperature gradient
  Frontal features
  “Cold Core”
“Superstorm”: March 1993
Hurricane Katrina: August 2005
Cyclones: Extratropical vs Tropical
L
Both can cause life threatening storm surge

## Slide 5: Employing Geographic Visualization to Convey Risk
Geovisualization – the creation and use of visual representations to facilitate thinking, understanding, and knowledge constructions about geospatial data (Nöllenburg, 2007)
“The human visual system is the most powerful processing system known” (Buckley et al., 2000)

## Slide 6: The Need for Visualization
Irene and Sandy Service Assessments
  Conveying storm surge information was extremely difficult
“The storm surge forecast was excellent but we are missing the ability to communicate it more visually”
“Mayor Bloomberg asked me every time, ‘If I walk out of my door, how far will the water be up on my legs’ ...He doesn’t want to know 12 feet, 8 feet, etc.... The more you can give me about the impact of surge by area—that would be helpful. Graphical inundation forecasts would be helpful.”
“there is considerable confusion on what the datums mean in terms of real world impacts.”
“There were forecasts, but there were no details about what the predicted surges would cause…There was no wording in the warning like, ‘Most of lower Manhattan will be under water at a certain point’ or ‘Staten Island will flood up to Beach Street.’”

## Slide 7: Coastal Population Density
Increasing population density along the U.S. Coast
Sea Level Rise
Santa Monica, CA
Source: The Third National Climate Assessment, 2014
Source: The Third National Climate Assessment, 2014

## Slide 8: Vertical Datums
Orthometric, Ellipsoidal and Tidal
  Tidal = Related to particular stages of ocean tide

## Slide 9: The Battery, NYC

## Slide 10: Storm Surge vs Storm Tide
Storm Tide = Astronomical Tide + Storm Surge
Storm surge = an abnormal rise of water generated by a storm, over and above the predicted astronomical tide level

## Slide 11: Storm Surge/Tide - Sandy
Storm surge is often the greatest threat to life and property from a tropical or extra-tropical storm
13.9 ft
Storm Tide
4.7 ft Normal High Tide
9.2 ft Surge
Storm Tide = Astronomical Tide + Storm Surge
Complex hazard, difficult to convey without visualization tools

## Slide 12: NWS Products
Tropical
Extratropical

## Slide 13: METHODOLOGY

## Slide 14: Study Area

## Slide 15: Digital Elevation Model
Post-Sandy DEM
Horizontal Coordinate System: NAD83, 1/9 Arc Second
Vertical Coordinate System: NAVD88, meters

## Slide 16: Storm Tide Data
Extract Total Water Level (TWL) grid from NWS’ Graphical Forecast Editor (MLLW, Feet)
Geospatial Data Abstraction Library (GDAL)
Graphical Forecast Editor

## Slide 17: VDatum
TWL grid (MLLW/feet) DEM (NAVD88/meters)

## Slide 18: Geoprocessing
Euclidean Allocation Extract overland
Resample
Raster Calculator Inundation (“bathtub approach”)
Spatial Analyst Convert units (meters to feet)
Resampled EA raster
Post VDatum raster

## Slide 19: RESULTS

## Slide 20: Results

## Slide 21: Results

## Slide 22: FUTURE WORK

## Slide 23: Future Work
Compare other impacts to inundation results
Automate processing
Minor to moderate coastal flooding event
Web interface

## Slide 24: THANK YOU!
adrienne.leptich@noaa.gov

## Slide 25: References
Buckley, Aileen R, Mark Gahegan, and Keith Clarke. 2000. "Geographic visualization." Emerging Themes in GIScience Research.
Nöllenburg, Martin. 2007. "Geographic Visualization." In Human-Centered Visualization Environments, edited by Andreas Kerren, Achim Ebert and Jörg Meyer, 257-294. Springer Berlin Heidelberg.