## Slide 1: ArcGIS Decision Support Tool for Infrastructure Improvement
ELSIT MANDAL (Penn State MGIS Candidate)
Road Systems Engineer, GIS Unit, Bureau of Transportation Planning
Kansas Dept. of Transportation

## Slide 2: ArcGIS Decision Support Tool for Infrastructure Improvement
Presentation Outline
Background & Data Analysis
Goals
Methodology & Approach
The Decision Support Tool Set
Conclusions & Outlook

## Slide 3: Freight Corridors of Significance
Credit: KDOT/Kansas Freight Advisory Committee (2014)

## Slide 4: Bridges: Posted, Restricted or Vertical Clearance Limited
This material is protected from discovery and admission into evidence in litigation pursuant to 23 USC 409. KDOT makes no warranties, guarantees, or representations for accuracy of this information and assumes no liability for errors or omissions.
Credit: KDOT

## Slide 5: Safety-Oversize Overweight (OSOW) Trucks
Credit: FHWA; https://safety.fhwa.dot.gov/geometric/pubs/mitigationstrategies/chapter3/3_verticalclearance.cfm
KTRIPS OSOW Terminology
Truck /Load Dimensions
Height > 14’ OR
Weight > 40T OR
Length > 120’ OR
Width > 8 ‘ 6 ”
KTRIPS*: Kansas Intelligent Truck Routing System

## Slide 6: Analysis/Classification of OSOW Data
Oversize Overweight (OSOW) Routes Geometry Available from KTRIPS Summary Classification of Data for 2 Years

## Slide 7: Analysis/Classification of OSOW Data
Oversize Overweight (OSOW) Routes Geometry Available from KTRIPS Grouped Classification of Data for 2 Years

## Slide 8: Analysis of OSOW Data: Origin and Destination (OD) Pairs

## Slide 9: Goals
Project Prioritization

## Slide 10: Goals
Develop Tools To:
  Analyze OSOW Truck Routes
  Help Visualize the Data
  Support Objective Decision Making
  Provide Easy to Use & Easily Modifiable Tools
  Provide Prioritized List of Bridges for Improvement Projects

## Slide 11: Methodology & Approach
Network Analyst

## Slide 12: Methodology & Problem Solving Using Network Analyst
Required:
ArcGIS Network Analyst Extension
Routable Network Dataset (Used ESRI Data & Maps: StreetMap North America Dataset)
Origin & Destination (OD) Pairs: Point Features
Barrier Bridges- Point Features Snapped to Network Dataset
Optional:
OSOW Truck Route Geometry

## Slide 13: Network Data Set Properties

## Slide 14: Approach--Network Analyst Route Solver--3 Step Process
Step1: No Barrier Route Solve
  Find Shortest Path Geometry & Travel Length
*Test Data Used for Illustration of Methodology

## Slide 15: Methodology-Route Solver Process Step2-Route Solve with Barriers
  Determine Barriers Specific to the OD pair
  Solve Route if Barriers Present on Shortest Path; Get New Route Length
  Select Barrier Bridges intersecting Shortest Path
  Assign Additional Miles Travelled to Intersecting Barriers as ‘ExtraMiles’ (314-264=50)
  Analyze all OD Pairs, Prioritize Barriers Based on Highest Accumulated ExtraMiles
*Test Data Used for Illustration of Methodology

## Slide 16: Methodology-Route Solver Process Step3
Step3: Barrier Solve After Removing Priority Barriers
  Re-calculate Travel Length Cost for the OD Pairs to Validate-Saved Miles (314-302)
*Test Data Used for Illustration of Methodology

## Slide 17: Computation Time Issues: Approach
Reduce Number of OD Pairs to be Analyzed: Total 148,000
  Grouping by Spatial Locations & by OSOW Load Characteristics: 47,579
  OD Lines Frequency >4: 3914
Reduce Size of Network Data Set
    Extract State Highway Segments Only 6 Sec. to 3 Sec. per OD Pair
    Apply ‘Dissolve’ on the Extracted Subset (No Barrier Solution)
Use OSOW Route Geometry for ‘With Barrier Route Solution’: This can Bypass Step2 Process

## Slide 18: The Decision Support Tools
Python Scripts

## Slide 19: Python Script Tools

## Slide 20: Analyze OSOW Data
Derive OD pairs, Classify Interstate, Inbound, Outbound & Intrastate
INPUTS: KTRIPS Routes, State Boundary Polygon
OUTPUTS: Origins, Destinations, OD Lines Frequency Polygon with Traffic Class

## Slide 21: Analyze OSOW Data
Derive OD pairs, OD Lines, Classify Interstate, Inbound, Outbound and Intrastate Traffic

## Slide 22: Step1:Route Solve -No Barriers Case
INPUTS: Origins, Destinations
OUTPUT: Shortest Path Route Feature Class

## Slide 23: Step2-Route Solve With All Barriers
INPUTS: Origins, Destinations, Barriers, Shortest Path Route
OUTPUTS: Alternative (Longer due to Presence of Barriers) Route Path
Prioritized Barriers

## Slide 24: Step3-Route Solve With Priority Barriers Removed
INPUTS:
Origins
Destinations
Barriers
Shortest Path Route
OUTPUTS:
Route Path with Lesser Number of Barriers, Prioritized Barriers

## Slide 25: List of Priority Bridges

## Slide 26: Bridge Improvement Projects Prioritization

## Slide 27: Conclusions & Outlook
The Tool Provides Insight for Planning Purposes
Provides Spatial Data Analysis /Visualization
Creates Prioritized Initial List of Bridges
Makes it Possible to Validate/Evaluate the Priority List
Further Work
  Run the Tool for Different Datasets for Further Evaluation
  Categorize OD Pairs To Explore Monthly/Seasonal Patterns
  Further Explore Ways to Reduce Computation Time
  Investigate Effect of Grouping of Bridges in Barrier Removal
  Different Methods of Applying Cost of Barrier
    Divide the Extramiles by Total number of Barriers
    Use Ton-Miles Instead of Miles
**The Tool Scripts will be Provided for Download on GitHub**

## Slide 28: Acknowledgements
Penn State MGIS program: Dr. Jan Wallgrun, Capstone Project Advisor
KDOT: Kyle Gonterwitz, P.E, GISP GIS Manager
                David Schwartz, P.E, Asst. Director, Planning & Development
                David Cronister, Planner, Models/ Forecasting
                Tina Cramer, GIS Application Developer
                John Culbertson, P.E, Bridge Evaluation Engineer
        John Maddox, Freight/Rail Manager
        Melinda Desch, P.E, Asst. Bureau Chief, Bureau of Program & Project Management

## Slide 29: Questions?