## Slide 1: Exploring Optimal GPS Signals for Autonomous Vehicles
Christopher Miller

## Slide 2: Overview
Background
    Motivation
    Autonomous Vehicle (AV) Requirements
Methodology
    Area of Concentration
    Data Inputs
    Obstacles with Visibility
Results
    New Methodology
    Solar Radiation Analysis
    Viable Roads
Reflections and Conclusion

## Slide 4: Background: Motivation
1.3 billion currently to 2 billion in 2030

## Slide 5: Background: Motivation

## Slide 6: Background: AV Requirements
Automated Driving System:
“hardware and software that are collectively […] used specifically to describe a level 3, 4, or 5 driving automotive system” - SAE International, 2018a

## Slide 7: Background: AV Requirements

## Slide 8: Background: AV Requirements
Lidar System

## Slide 9: Background: AV Requirements

## Slide 10: Methodology: Area of Concentration
Washington, D.C.
Access to data – opendata.dc.gov
Infrastructure – future integration potential
Interest within the City –
        Need to improve
        Member of an initiative group

## Slide 11: Methodology: Data Inputs
Visibility Tool in ArcMap
  Surface elevation raster – (DSM)
  digital surface model,
  Observer features of satellite data,
  Observer Elevation

## Slide 12: Methodology: Data Inputs
Visibility Tool in ArcMap
  Surface elevation raster – (DSM)
  digital surface model,
  Observer features of satellite data,
  Observer Elevation

## Slide 13: Methodology: Data Inputs
Visibility Tool in ArcMap
  Surface elevation raster – (DSM)
  digital surface model,
  Observer features of satellite data,
  Observer Elevation

## Slide 14: Methodology: Data Inputs
  Observer features of satellite data
  Almanac – easy to use .txt files, but less accuracy and additional calculations
  Broadcast Ephemerides – more accurate but harder to use
  Precise Ephemerides – most accurate

## Slide 15: Methodology: Data Inputs
Conversion into geodetic –
Latitude, longitude and altitude: NGS’s NCAT
Precise Ephemerides –
XYZ geocentric coordinates of satellites

## Slide 16: Methodology: Data Inputs
Setup –
  Observer Features: 32 GPS Satellite Locations, 3 times and 3 days => 285 coordinates*
  Height: Average altitude/Visibility run
  Test Run –
  Observer Features: 1 Satellite Coordinate
  Height: Set to 20,200,000 meters
*should have been 288 but some satellites were unavailable

## Slide 17: Methodology: Data Inputs
Setup –
  Observer Features: 32 Satellite Locations 3 times and 3 days => 288 coordinates
  Height: Average altitude/Visibility run
  Test Run –
  Observer Features: 1 Satellite Coordinate
  Height: Set to 20,200,000 meters (12,550 miles)

## Slide 18: Methodology: Obstacles with Visibility
Workflow –
  Visibility tool on closest satellite coordinate
259 miles

## Slide 19: Methodology: Obstacles with Visibility
Workflow –
  Visibility tool on closest satellite coordinate
  Line-of-Sight Across Large Distances => Mosaic DSM

## Slide 21: Methodology: Obstacles with Visibility
Workflow –
  Visibility tool on closest satellite coordinate
  Line-of-Sight Across Large Distances => Mosaic DSM
  Observer Height Too High => Test within DSM

## Slide 22
1,000 Meters
10,000 Meters
100,000 Meters

## Slide 23: Results: New Methodology
Visibility Tool unable to produce results

## Slide 24: Results: New Methodology
Visibility Tool unable to produce results
Alternative: Area Solar Radiation Analysis –
  Inputs: DSM, Sky size and time configuration

## Slide 25: Results: New Methodology
Visibility Tool unable to produce results
Alternative: Area Solar Radiation Analysis –
  Inputs: DSM, Sky size and time configuration
  Obstacles
“solar modeling in GIS is a very intensive geoprocessing (computational time) process” which, on a single simulation “can range from a few hours up to multiple days” (Chow, 2014)

## Slide 26: Results: New Methodology
Visibility Tool unable to produce results
Alternative: Area Solar Radiation Analysis –
  Inputs: DSM, Sky size and time configuration
  Obstacles
  Solution – Modify Resolution

## Slide 27: Results: Solar Radiation Analysis
Troubleshooting Inputs
DSM Resolution | Sky Size (Resolution) | Time configuration | Result | Output Available
1-meter | 200 | 2 days: 1/5/21 until 1/6/21 | >48 hours | N
1-meter | 2,800 | 3 days | >24 hours | N
1-meter | 10,000 | 3 days | >16 hours | N

## Slide 28: Results: Solar Radiation Analysis
Troubleshooting Inputs
Output Available!
DSM Resolution | Sky Size (Resolution) | Time configuration | Result | Output Available
1-meter | 200 | 2 days: 1/5/21 until 1/6/21 | >48 hours | N
1-meter | 2,800 | 3 days | >24 hours | N
1-meter | 10,000 | 3 days | >16 hours | N
10-meter | 2,800 | 3 days | 12.5 hours | Y
30-meter | 2,800 | 3 days | 1.5 hours | Y

## Slide 31: Results: Viable Roads
High Solar Radiation = Visible Area

## Slide 32: Results: Viable Roads
High Solar Radiation = Visible Area
Replicate Across all D.C. roads
Major Roads
 | Total DSM | all roads | major roads
not visible | 3% | 2% | 3%
some visibility | 18% | 17% | 13%
visible | 79% | 81% | 84%

## Slide 34: Results: Reflections and Conclusion

## Slide 35: Results: Reflections and Conclusion
Limitations
Line-of-sight – Building Height in other cities
Other urban canopy obstructions
Opportunities
GPS Signal Enhancers
Other software, computer, users
Signal Quality Importance

## Slide 36: Results: Reflections and Conclusion
Limitations
Line-of-sight – Building Height in other cities
Urban canopy obstructions
Opportunities
GPS signal enhancers
Other software, computer, users
Signal Quality Importance

## Slide 37: Results: Reflections and Conclusion
Limitations
Line-of-sight – Building Height in other cities
Urban canopy obstructions
Opportunities
GPS Signal Enhancers
Other software, computer, users
Signal Quality Importance

## Slide 38: Exploring Optimal GPS Signals for Autonomous Vehicles
Christopher Miller

## Slide 39: References
Adali, Erkan et al. (2018). Detecting Road Lanes under Extreme Conditions: A Quantitative Performance Evaluation. 2018 6th International Conference on Control Engineering & Information Technology (CEIT). Retrieved in November 10, 2019 from https://ieeexplore-ieee-org.ezaccess.libraries.psu.edu/document/8751835.
Adjrad, Mounir, et al. (2019). Performance assessment of 3D‐mapping‐aided GNSS part 2: Environment and mapping. Navigation, Volume 66, Issue 2. Retrieved in November 10, 2019 from https://onlinelibrary-wiley-com.ezaccess.libraries.psu.edu/doi/full/10.1002/navi.289.
Chow, Annie. et al. (2014). GIS Modeling of Solar Neighborhood Potential at a Fine Spatiotemporal Resolution. Buildings. Retrieved in February, 2021 from https://www.mdpi.com/2075-5309/4/2/195/htm.
DMPED. (2019). Autonomous Vehicles Working Group. DC.gov. Retrieved on November 9, 2019 from https://dmped.D.C..gov/page/autonomous.
El-naggar, Aly. (2012). New method of GPS orbit determination from GCPS network for the purpose of DOP calculations. Alexandria Engineering Journal. Retrieved on December 9, 2019 from https://www.sciencedirect.com/science/article/pii/S1110016812000464#t0020.
ESRI. (2016a). An overview of the Solar Radiation tools. ArcMap. https://desktop.arcgis.com/en/arcmap/10.3/tools/spatial-analyst-toolbox/an-overview-of-the-solar-radiation-tools.htm.
ESRI. (2016b). Area Solar Radiation. ArcMap. https://desktop.arcgis.com/en/arcmap/10.3/tools/spatial-analyst-toolbox/area-solar-radiation.htm.
Federal Highway Administration. (2007). Mitigation Strategies for Design Exceptions. Department of Transportation. Retrieved on April 20, 2021 from https://safety.fhwa.dot.gov/geometric/pubs/mitigationstrategies/chapter3/3_lanewidth.cfm.
Filgueira, A. et al. (2017). Quantifying the Influence of Rain in Lidar Performance. Measurement, Volume 95. Retrieved on October 18, 2019 from https://www-sciencedirect-com.ezaccess.libraries.psu.edu/science/article/pii/S0263224116305577.
Gossling, Stefan. (2017). The Automotive System. The Psychology of the Car, Chapter 1, Pages 1-18. Retrieved on October 24, 2019 from https://www-sciencedirect-com.ezaccess.libraries.psu.edu/science/article/pii/B9780128110089000016.
Germroth, Matthew. et al. (2005). GIS and Satellite Visibility: Viewsheds from Space. 2005 ESRI International User Conference. Retrieved on December 9, 2019 from https://proceedings.esri.com/library/userconf/proc05/papers/pap1615.pdf.
GPS.gov. (2021). Space Segment. U.S. Air Force. Retrieved February, 2021 from https://www.gps.gov/systems/gps/space/.

## Slide 40: References (continued)
IGS. (2019). Access to Products. International GNSS Service. Retrieved on December 9, 2019 from https://kb.igs.org/hc/en-us/articles/115003935351.
Jin, Shuaggen, et al. (2014). GNSS Remote Sensing: Theory, Methods and Applications, Chapter 1, page 5. Springer Science and Business Media Dordrecht. Retrieved on December 4, 2019 from https://link-springer-com.ezaccess.libraries.psu.edu/book/10.1007%2F978-94-007-7482-7.
Kim, Dong, et al. (2019). Simple-Yet-Effective SRTM DEM Improvement Scheme for Dense Urban Cities Using ANN and Remote Sensing Data: Application to Flood Modeling. Integrated Flood Management: Concepts, Methods, Tools and Results. Retrieved on April 19, 2021 from https://www.mdpi.com/2073-4441/12/3/816/htm.
Luettel, Thorsten, et al. (2012). Autonomous Ground Vehicles—Concepts and a Path to the Future. IEEE, Special Centennial Issue. Retrieved on December 4, 2019 from https://ieeexplore-ieee-org.ezaccess.libraries.psu.edu/document/6179503.
Monaghan, Ryan. (2006). GPS Satellite Position Estimation from Ephemeris Data by Minimum Mean Square Error Filtering Under Conditions of Selective Availability. Retrieved on December 11, 2019 from http://citeseerx.ist.psu.edu/viewdoc/download?doi=10.1.1.297.6452&rep=rep1&type=pdf.
Navigation Center. (2019). GPS ALMANACS, NANUS, AND OPS ADVISORIES ARCHIVES. U.S. Department of Homeland Security. Retrieved on December 8, 2019 from https://www.navcen.uscg.gov/?Do=gpsArchives&exten=txt.
NCPC. (1998). PART I: HISTORICAL BACKGROUND ON THE HEIGHT OF BUILDINGS ACT. National Capital Planning Commission. Retrieved on December 10, 2019 from https://www.ncpc.gov/heightstudy/docs/Historical_Background_on_the_Height_of_Buildings_Act_(draft).pdf.
NGS. (2019a). NGS Coordinate Conversion and Transformation Tool (NCAT). NOAA. Retrieved in December, 2019 from https://www.ngs.noaa.gov/NCAT/.
NGS. (2019b). API for NGS’s Coordinate Conversion and Transformation Tool (NCAT). NOAA. Retrieved in December, 2019 from https://geodesy.noaa.gov/web_services/ncat/index.shtml.
Open Data D.C. (2019). 2018 Lidar – Digital Surface Model – Mosaic. District of Columbia GIS Program. Retrieved in November, 2019 from https://app.box.com/s/qedupea6k9cldn3l4b4eg9c2ajhtbxri.
Peng, D.J. (2014). The Effect of GPS Ephemeris on the Accuracy of Precise Orbit Determination of LEO Satellite-borne GPS. Chinese Astronomy and Astrophysics, Volume 33, Issue 2. Retrieved in December, 2020 from https://www-sciencedirect-com.ezaccess.libraries.psu.edu/science/article/pii/S0275106209000447#.
SAE International. (2018a). Taxonomy and Definitions for Terms Related to Driving Automation Systems for On-Road Motor Vehicles. Surfaced Vehicle Recommended Practice. Retrieved on November 11, 2019 from https://www.sae.org/standards/content/j3016_201806/preview/.

## Slide 41: References (continued)
SAE International. (2018b). SAE International Releases Updated Visual Chart for Its “Levels of Driving Automation” Standard for Self-Driving Vehicles. Retrieved on November 8, 2019 from https://www.sae.org/news/press-room/2018/12/sae-international-releases-updated-visual-chart-for-its-%E2%80%9Clevels-of-driving-automation%E2%80%9D-standard-for-self-driving-vehicles
Sickle, Jan Van. (2019). Geocentric Datum. GEOG 862: GPS and GNSS for Geospatial Professionals, Lesson 5: Geodetic Datums. Retrieved on December 11, 2019 from https://www.e-education.psu.edu/geog862/node/1798.
U.S. Census Bureau. (2019). Route Type Codes and Definitions. Census.gov. Retrieved on April 20, 2021 from https://www.census.gov/library/reference/code-lists/route-type-codes.html.