## Slide 1: Tracking Pluvial-Related Expansion and Contraction of Water Bodies in the South Dakota Prairie Pothole Region Using the Landsat Record with an Object-Based Image Analysis Approach
MGIS Capstone Proposal
Nathan Roberts
Notes: Good.

## Slide 2: Presentation Outline
Background
Study Area
Project Goals and Objectives
Methodology
Initial Results
Future Directions

## Slide 3: Background: Prairie Pothole Region (PPR)
Land Area: 900,000 km2
Landscape includes depressions and low spots formed by glaciers
90% of private land classified as agriculture
Important habitat and flyway for birds
Landscape and land use susceptible to changes in climate especially to extreme changes in precipitation

## Slide 4: Background: Climate Pluvial Years
Pluvial Month: precipitation exceeds 40% of monthly average (Findell and Delworth 2010)
PPR experienced pluvial precipitation during early 1990s
Resulted in formation and expansion of waterbodies
Flooded farmland, roads, and towns
Past studies have examined PPR response to pluvial precipitation but at smaller scales

## Slide 5: Background: Current Climate Conditions
Climate data proposes PPR is now experiencing dry conditions
Current year to date precipitation amounts indicate PPR is in drought conditions
Field inspection suggests water bodies are retreating

## Slide 6: Study Area: South Dakota PPR
South Dakota PPR: ~65,107 km2
Dominated by row crop and pasture land
Composes almost all the suitable row crop production ground in the state
Agriculture has a $25 billion dollar annual impact on the state
Any disruption to agriculture or new means of management can have a profound effect

## Slide 7: Research Question
Are areas that have been reclaimed from water bodies being farmed and if so what is being grown?

## Slide 8: Project Goals and Objectives
Quantify farmland lost or gained to pluvial water bodies within the South Dakota PPR from 1986 to 2016
Quantify spatial/temporal relationships between the expansion and contraction of pluvial water bodies and precipitation received from 1986-2016
Determine what crops are currently being produced in areas that have seen pluvial water body retreat
Develop an automated framework for future studies involving large datasets within the PPR

## Slide 9: Methods: Data Required
Dates | Spacecraft | Sensor | Resolution | Coordinate System
1986 to 1999 | Landsat 5 | TM | 30 Meters | UTM Zone 14N
2000 to 2012 | Landsat 7 | ETM+ | 30 Meters | UTM Zone 14N
2013 to 2016 | Landsat 8 | OLI | 30 Meters | UTM Zone 14N
Landsat scenes from 1986 to 2016 used to construct an annual Landsat time series for the AOI
Scenes captured in June, July or August to correspond with peak growing season
Less than 10% cloud cover required
Sample Landsat Image

## Slide 10: Methods: Data Required
Dataset | Description | Resolution | Years Available | Type | Source
NASS CDL | Crop Cover | 30 Meters | 2006 to 2016 | Grid | USDA
NLCD | Land Cover | 30 Meters | 2011 | Grid | MRLC
PRISM Climate Data | Climate | 800 Meters | 1895-2016 | Grid | PRISM Group
Additional Datasets

## Slide 11: Methods: Pre-Processing
Acquire Landsat scenes
Acquire NASS CDL
Acquire NLCD
Create Composite Band Rasters TM/ETM+
Create Composite Band Rasters OLI
Mosaic Rasters into 1 image
Clip to AOI
Clip to AOI
Clip to AOI
Reclassify:
Open Water, Crops, Wetlands, Developed, Grassland/Pasture
Mosaic Rasters into 1 image
Clip to AOI
Create Clipped Composite Raster
Create Clipped Composite Raster
Create Clipped Reclassified NLCD
Create Clipped CDL

## Slide 12: Methods: Object Based Image Analysis
Source Image
Segmented Image
Objects classified into groups
Segments image into objects based on like pixels
Used extensively to detect change in forest and crop lands

## Slide 13: Methods: Landsat Water Index Calculations
Water classified objects merged into region
Water bodies identified using Normalized Difference Water Index (NDWI) (McFeeters 1996)
Calculated as:
Objects with NDWI < zero = no water
Objects with NDWI > Zero = water

## Slide 14: Methods: Landsat Classification
Water body extraction workflow
Create composite band raster for each Landsat scene
Clip composite band raster to AOI
Acquire Landsat scenes
Green: Data Acquisition
Blue: ArcGIS
Tan: eCognition
Yellow: Fieldwork
Classification
Bin water bodies to classes perm/seasonal
Segmentation
Calculate NDWI
Assign Objects w/ NDWI > 0 “Water”
Assign Objects w/ border >. 5 “Water”
Merge Objects “Water”)
Compare NDWI Values
Export Shapefile
Visual inspection and correction
Field Ground Truth
Final Classification
Accuracy Assessment

## Slide 15: Methods: Data Integration
Water Body Polygons
CDL
NLCD
Over lay
Over lay
Calculate Crop Types Present in water areas
Calculate Land Area Changes
PRISM Climate Data
Correlate water Body with precip. data
Notes: Fix Arrows. 20 minute mark

## Slide 16: Initial Results: Landsat Classification
Example digitized slough over three years near Langford, South Dakota as depicted in 1986, 1995 and 2016.

## Slide 17: Initial Results: Accuracy Assessment
Year | Correctly Classified Water Pixels | In Correctly Classified Water Pixels | Correctly Classified Non-Water Pixels | In Correctly Classified Non-Water Pixels | Users Accuracy Water Class (Com) | Users Accuracy Non-Water Class (Com) | Producers Accuracy Water Class (OM) | Producers Accuracy Non-Water Class (OM) | Total Accuracy
1986 | 3 | 0 | 46 | 1 | 100% | 98% | 75% | 100% | 98%
1995 | 4 | 3 | 39 | 4 | 57% | 91% | 50% | 93% | 86%
2016 | 1 | 2 | 47 | 0 | 33% | 100% | 100% | 95% | 95%
Notes: Build out the the slide
Users=Error of Commission
Producer error of ommission

## Slide 18: Initial Results: Waterbody Advance and Retreat
Test area near Langford, South Dakota
Surface area was calculated as 318 hectares, 1,315 hectares and 518 hectares respectively
Precipitation time series diagram

## Slide 19: Initial Results: Crop Distribution
Crops now grown in previously flooded areas in 1995
10 km study area
Crop | Hectares (ha)
Soy Beans | 24
Hay | 23
Corn | 20
3,568 of 41,756 ha flooded
998 ha re-claimed

## Slide 20: Future Directions
Refine methods
Mask cloud pixels
Automate processing
Correlate water body advance/retreat to climate data
Predict crop distribution

## Slide 21: Questions?