## Slide 1: AMBUSH VULNERABILTY MODEL DEVELOPMENT
John William Shinsky
john.w.shinsky2.civ@mail.mil

## Slide 2: Problem Statement
Is line-of-sight enough to analyze a vehicles vulnerability to an attack?
  Speed?
  Continuous line-of-sight?
  Kill Chain Sequence Time?
Goal: Improve current methodology to incorporate vehicle speed, target acquisition time, and continuous line-of-sight to better analyze a moving target.

## Slide 3
Current AMSAA Model: Overhead Angle of Attack Model
Original Problem: Locate and characterize overhead firing opportunities
Programming Language: Python uisng ArcGIS
Current Model
LIDAR
Route Points
Compute viewshed and point summaries at each individual point
Excel Summary Table
Viewshed for each point

## Slide 4
Identifies every point the vehicle can see and be seen by a 2m tall firer above the vehicle (>1° angles).
Viewshed Analysis
0:7,000

## Slide 5
Angle and distance are calculated for every visible point (>1° angles).
Higher angles represent a threat from a higher vantage point.
Green = 1-7°
Yellow = 7-14°
Red = 14-80°
Angle and Distance Calculation
0:7,000

## Slide 6
Threat occurrences over total firing opportunities
Averaged over all route points.
Table for distribution.
Statistical Aggregation

## Slide 7
Static Minimum Range
Static Maximum Range
Requires Route Points
Stationary Target
Statistical Aggregation
Key Limitations
Weapons Systems
Different Vehicles
Operational Usage
Non Military Usage

## Slide 8
Proposed Model: Ambush Vulnerability Model
Problem: Locate attack threat positions for a moving target
Programming Language: Python using ArcGIS
Proposed Model
LIDAR
Route
Vehicle Length
Vehicle Speed
Target Acquisition Time
Split route into evenly spaced points
Determine how many route points must be visible for a viable threat
Compare to last viewshed to establish continuous line of sight
Compute viewshed at individual point
Find locations that have had line of sight for the specified number of points
Add all line of sight rasters to get a final raster showing all viable threats
Final Viable Threat Map
Iterative Multiple Viewshed Analysis
Repeat For Next Point

## Slide 9: Proposed Methodology
Kill Chain Sequence Time (Acquire, Aim, Fire, Hit)
Multiple Viewshed Analysis
Minimum Range
Maximum Range
Sample Distance
Vehicle Speed

## Slide 10: Multiple Viewshed Analysis
Current Viewshed
Previous Viewshed
Line Of Sight Raster
nth Viable Threat Raster
1st Viable Threat Raster
All Threats Final Output
+ 2nd + 3rd + ...
Factor In User Defined Kill Chain Sequence Time
0:5,000
0:5,000
0:5,000
0:5,000
0:5,000
0:5,000

## Slide 11: Expected Results
Drastic decrease in the number of threat locations.
Firing opportunities on side streets will not be as viable of a threat
Problem areas will be points along the road and on top of nearby buildings

## Slide 12: Literature Review
  Weapons Fan Algorithm (Guth, 2003)
  US Naval Academy
  Uncertainty in Viewshed Analysis (Raehtz, 2011)
  Michigan State University
  Cumulative Viewshed Analysis (Wheatley, 1995)
  University of Southampton
  Archaeology (Ruggles, 1993)
  University of Leicester

## Slide 13: Conclusion
The proposed model will allow for a larger range of applications.

## Slide 14: Questions
The ability to determine the threat of an overhead attack to a moving target gives the model the capability to be useful for operational planning
The proposed model also allow the capability of non military uses

## Slide 15: References
Guth, P.L. (2003). Ambush Movies and the Weapons Fan Algorithm: Military GIS Operations and Theory, in Proceedings of the International Conference on Military Geology and Geography, June 15-18, 2003, West Point NY.
Guth, P.L. (2004). The Geometry of Line-of-Sight and Weapons Fan Algorithms: in Caldwell, D.R., Ehlen, J., and Harmon, R.S., eds., Studies in Military Geography and Geology, Dordrecht, The Netherlands, Kluwer Academic Publishers, chapter 21, p.271-285.
Raehtz, S.M. (2011). Accounting for Uncertainty in Viewshed Analysis of IED Ambush Sites in Afghanistan. Michigan State University. Retrieved August 20, 2014, from http://etd.lib.msu.edu/islandora/object/etd%3A1141
Ruggles, C.L.N., Medyckyj-Scott D.J., and Gruffydd A. (1993). Multiple Viewshed Analysis Using GIS and Its Archaeological Application: a Case Study in Northern Mull, in: Andresen, J., T. Madsen and I. Scollar (eds.), Computing the Past. Computer Applications and Quantitative Methods in Archaeology. CAA92. Aarhus University Press, Aarhus, pp. 125-132.
Wheatley, D. (1995). Cumulative Viewshed Analysis: A GIS-Based Method for Investigation Intervisibility, and its Archaeological Application. In Lock & Stancic (Eds.), Archaeology and Geographical Information Systems, 171-186. Taylor and Francis: London.