## Slide 1: Visualizing Land Use Changes based on Historic Images of Brevard County, Florida
Marnie Sippel, MGIS Candidate
Penn State University GEOG 596A
May 5, 2014
Advisor: Dr. Jay Parrish

## Slide 2: Capstone Presentation Overview
Project Objective
Study Area
Historic Aerial Photo Sources & Years
Research of Potential Software for the County
Methodology for determining Land Use Changes
Project Challenges
Web Deployment
Project Timeline

## Slide 3: Project Objectives
Research potential software for Brevard County to utilize on County-wide historic aerial project and make a recommendation for the software.
Test potential software on small study area (6 x 6 miles).
Produce a user guide to be used by other county GIS volunteers to develop countywide historic aerial layers.
Manually determine land change usage from 1943 to 2007 for my study area. (1943, 1969, 1983, 2007)

## Slide 4: Study Area

## Slide 5: Study Area
Source: Brevard County Property Appraiser Office https://www.bcpao.us/

## Slide 6: Study Area

## Slide 7: Historic Aerial Photos Sources/Years
1943 – University of Florida
1958 – University of Florida
1969 – University of Florida
1979 – University of Florida
1983 - Florida Department of Transportation
1993 - Florida Department of Transportation
2007 – Brevard County
2012 - Florida Department of Transportation

## Slide 8: University of Florida
Flight Path Map with link to Photo

## Slide 9: Florida Dept of Transportation
Thankfully, FTP downloads with Township and Range numbers are available by request

## Slide 10: Research of Potential Software
ESRI - ArcMap
Exelis - ENVI
Intergraph - ERDAS Imagine
Clark University- IDRISI
PCI GeoMatics – Historic Airphoto Processing
Blue Marble - Global Mapper

## Slide 11: ArcMap Automatic Georeferencing

## Slide 12: ArcMap - Manual Georeferencing
At least 12 control points

## Slide 13: Flight Path Overlap
Multiple Photos Needed for Study Area

## Slide 14: ArcMap Workflow
For each of the selected 7 years:
Clip Photos
Georeference photos for study area
Mosaic photos into one file per year
Land Use Analysis for 4 years (1943, 1969, 1983, 2007):
Digitize each land use type
Assign land use type as an attribute
Dissolve feature class per year based on classification
Summarize land classification types per year
Determine percent change from decade to decade

## Slide 15: Methodology for determining Land Use Change
Manual Classification of digitized polygons
  Personal judgment/bias
  Scale and Accuracy of digitization process
Classifications:
  Developed Land – residential, streets, industrial, non-natural areas
  UnDeveloped Land – green areas, natural areas
  Water – man-made or natural bodies of water that are not the river
  River

## Slide 16: Final ArcMap
1969
2007
1969
Developed Land = 13%
Undeveloped Land = 86%
Inland Water = 1%
2007
Developed Land = 20%
Undeveloped Land = 64%
Inland Water = 16%

## Slide 17: Better Workflow?
Exelis - ENVI
Intergraph - ERDAS Imagine
Clark University- IDRISI
PCI GeoMatics – Historic Airphoto Processing
Blue Marble - Global Mapper
……that is the question.

## Slide 18: Project Challenges
An enormous amount of manual labor to georeference the whole county for each year.
Quality Control and Assurance of digitization process.
  Bias when visually digitizing land use.
  Enlist students/volunteers to assist with digitization process on 3 tiles in each time period. Compare differences in classification to assess accuracy of classification levels.
Are Orthorectified photos necessary?

## Slide 19: Web Deployment
Publish map service and deploy through ArcGIS Server on EC2 as a tiled cache.
Use ArcGIS Viewer for Flex to create online map.
Include Time Slide bar for users to change photo images by year.

## Slide 20: Anticipated Results
A paper that supports the recommendation of software for the Brevard County historic aerial photo project.
Development of a “user-manual” for County volunteers to continue the historic aerial photo project.
Development of a sample website to demonstrate to the County the potential visualization of land use changes.
Land Use Analysis: expectation of seeing a significant increase in developed land from 1943 to 2012.

## Slide 21: Project Timeline
May
  Test/Analyze Software options
June
  Georeference photos of study area for each time period
July
  Manual Classification of study area
August
  Analysis of Land Change
  Deploy website with disclaimers
  Develop User’s Guide
September/October
  Presentation

## Slide 22: Presentation Possibilities
Central Florida GIS Workshop Sept 15 – 16, 2014
Orlando, FL
Abstract Due: July 1
South Florida GIS Expo Oct 2 -3, 2014
West Palm Beach, FL
Abstract Due: date not published yet
Applied Geography Conference Oct 15 – 17, 2014
Atlanta, GA
Abstract Due: June 6

## Slide 23: Acknowledgements
Dr. Jay Parrish, Advisor
Brevard County Dept of Natural Resources, FL

## Slide 24: Sources
Brevard County Department of Natural Resources (2014). http://www.brevardcounty.us/NaturalResources/Home
Brevard County Property Appraiser (2014). https://www.bcpao.us/
DiBiase, David (2014). GEOG 482: Nature of Geographic Information. Chapter 8, pg. 19. Classifying Landsat Data for the National Land Cover Dataset. Retrieved from https://www.e-education.psu.edu/natureofgeoinfo/c8_p19.html
ESRI ArcGIS Resources. (2012, June 20). How time is supported in spatial data. Retrieved from:
http://resources.arcgis.com/en/help/main/10.1/index.html#/How_time_is_supported_in_spatial_data/005z00000004000000/
ESRI ArcGIS Resources. (2013, Dec 17). ArcGIS Viewer for Flex. Retrieved from:
http://resources.arcgis.com/en/help/flex-viewer/concepts/index.html#//01m30000003n000000
ESRI Video. (2014). Improved Georeferencing Workflows in ArcGIS 10.1. Retrieved from: http://video.esri.com/watch/1924/improved-georeferencing-workflows-in-arcgis-101
Florida Department of Transportation. (1996 – 2014). Surveying & Mapping, Get Aerials. Data Retrieved from: http://www.dot.state.fl.us/surveyingandmapping/aerial_get.shtm

## Slide 25: Sources
Florida Geographic Data Library. (2014) FGDL Metadata Explorer: Search & Download Data. Retreived from: http://www.fgdl.org/metadataexplorer/explorer.jsp
Multi-Resolution Land Characteristics Consortium (2014, Apr 11). National Land Cover Database 2011. Retrieved from: http://www.mrlc.gov/nlcd11_leg.php
University of Florida, George A Smathers Libraries (2004 – 2013). Aerial Photography: Florida, Flights By County. Data Retrieved from: http://ufdc.ufl.edu/aerials/all/table
USGS (1976). Anderson, et. al. Geological Survey Professional Paper 964. A Land Use and Land Cover Classification System For Use with Remote Sensor Data. Retrieved from: http://landcover.usgs.gov/pdf/anderson.pdf
USGS Land Cover Institute (2012, Dec). NLCD Land Cover Class Definitions. Retrieved from: http://landcover.usgs.gov/classes.php
Potential Software:
ESRI- http://www.esri.com/
ENVI - https://www.exelisvis.com/ProductsServices/ENVI/ENVI.aspx
ERDAS Imagine - http://www.hexagongeospatial.com/products/ERDAS-IMAGINE/Details.aspx
IDRISI - http://www.clarklabs.org/
PCI GeoMatics HAP - http://www.pcigeomatics.com/software/production-workflows
Global Mapper - http://www.bluemarblegeo.com/products/global-mapper.php

## Slide 26: Questions