## Slide 1: GIS for Reservoir Management: Estimating Original Gas In Place
Jeffrey Vu, M.GIS Candidate
Dr. Patrick Kennelly, Advisor
GEOG 596A Winter 2013

## Slide 2: Outline
Background
Introduction
Objectives
Data
Methods
Anticipated Results
Timeline
Future Development
References
Acknowledgements

## Slide 3: Background
What is reservoir management? Use of earth sciences and petroleum engineering to forecast and manage the recovery of oil and natural gas (hydrocarbons) in place from a field or a prospect
Reservoir management plays an important role in the oil and gas industry by evaluating the greatest economic recovery from a reservoir. - Increase oil and gas production - Decrease risk - Maximize recovery and minimize costs
Reservoir Engineers typically don’t use GIS. They normally use Microsoft Excel for all sorts of modeling, including analysis.

## Slide 4: Introduction
Volumetric estimation is the common technique of the geologists to calculate hydrocarbons in place based on geologic mapping and reservoir engineering data.
http://discoverygeo2com/Papers/Reservoir%20Eng%20for%20Geos%2032pdf
MMCF: Million Cubic Feet
OGIP: Original Gas In Place

## Slide 5: History and current process
Determine reservoir gas in place using BASIC programming language BASIC (standing for Beginner's All Purpose Symbolic Instruction Code)
Cranmer, John L.: “BASIC Reservoir Engineering Manual”, PennWell (1982) 24-25.

## Slide 6: History and current process (cont.)
Calculate original gas in place using Excel
http://petroleumsupport.com/volume-reservoir-and-gas-reserve-calculator-spreadsheet/
Calculate gas in place using Petra

## Slide 7: Current workflow
Petra
Geologists generate net pay, porosity, water saturation grids
ArcMap
PLSS sections
Generate centroids
Excel
Input Data
Calculate OGIP using formulas
Extract Values to Points
1320 sq.ft. x 1320 sq.ft. = 40 acres
PLSS section (640 acres)

## Slide 8: Objectives
Create a workflow using out-of-the-box tools in ArcToolbox as a screening workflow to estimate the Original Gas In Place (OGIP) for the Reservoir Engineers
Streamline the workflow to avoid human error in importing and exporting data
Allow user-drawn polygon as input to increase flexible analysis of fields or prospects
Use folder structure to manage data inputs and results
Run different scenarios
Estimate the OGIP under different uncertainties and assumptions

## Slide 9: Proposed workflow (using ArcGIS)
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
Water saturation
Porosity
Net pay
Grids exported from Petra
Intersected
40-ac fishnet
Average values
1320 sq.ft. x 1320 sq.ft. = 40 acres
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
Calculate OGIP
OGIP map
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .

## Slide 10: Data
Exported grids from Petra
Net pay grid is required
All input grids must have the same coordinate systems and cell sizes
User’s parameters

## Slide 11: Methods
Data management: User-defined folder structure
User-drawn polygon to increase flexibility in selecting areas of interest
Reusable workflow to run different scenarios
Python codes to check inputs (grid or constant value)
Is a grid?
YES
NO
Copy to project’s folder
Create a grid based on user-drawn polygon
User-drawn polygon
2 | 2 | 2 | 2
2 | 2 | 2 | 2
2 | 2 | 2 | 2
2 | 2 | 2 | 2
2 | 2
2 | 2
2 | 2
2 | 2
2 | 2 | 2 | 2
2 | 2
User’s input = 2

## Slide 12: Con (Spatial Analyst)
Performs a conditional if/else evaluation on each of the input cells of an input raster
Set raster cell to 0 when VALUE < 0
-5 | 12 | 26 | 50
34 | 19 | 44 | -10
48 | 42 | 64 | 12
2 | -15 | 24 | -47
0 | 12 | 26 | 50
34 | 19 | 44 | 0
48 | 42 | 64 | 12
2 | 0 | 24 | 0

## Slide 13: Reclassify
Reclassifies or changes the values in a raster
Set raster cells to NoData or 1
11 | 12 | 26 | 50
34 | 19 | 44 | 
48 | 42 | 64 | 22
2 | -15 | 24 | 0
1 | 1 | 1 | 1
1 | 1 | 1 | 
1 | 1 | 1 | 1
1 | 1 | 1 | 1
NoData

## Slide 14: Intersect & Fishnet Polygons
Convert all raster datasets to polygon features and intersect with each other
Create 40 acre fishnet polygons in Python
Water saturation
Porosity
Net pay
Intersected fishnet polygons
1320 sq.ft. x 1320 sq.ft. = 40 acres

## Slide 15: Zonal Statistics as Table
Create additional fields in the fishnet polygons feature class
Run “Zonal Statistics as Table” tool for all input grids
. | . | . | .
. | . | . | .
. | . | . | .
. | . | . | .

## Slide 16: Join Tables
Join “Zonal Statistic” tables to fishnet polygons table
Remove join before joining another table

## Slide 17: Calculate Fields
Calculate fields, including OGIP
OGIP Polygons

## Slide 18: OGIP Raster
Create OGIP centroids
Generate OGIP raster grid
Create OGIP contours

## Slide 19: Anticipated Results
Table with calculated of OGIP
OGIP grid
OGIP contour map
bcf
(billion cubic feet)

## Slide 20: Timeline
Collect Data
OGIP Formula
Python Scripts
Model Builder
Test
CalGIS
January 2014
February 2014
March 2014
April 2014

## Slide 21: Future Development
Calculate remaining gas in place
Calculate net revenue interest by leases automatically

## Slide 22: References
Reservoir Engineering for Geologists http://discoverygeo.com/Papers/Reservoir%20Eng%20for%20Geos%203.pdf
Cranmer, John L.: “BASIC Reservoir Engineering Manual”, PennWell (1982) 24-25.
Volume Reservoir and Gas Reserve Calculator Spreadsheet http://petroleumsupport.com/volume-reservoir-and-gas-reserve-calculator-spreadsheet
Basic Geology and Volumetric Analyses http://www.petrocenter.com/reservoir/re01.htm
ArcGIS 10.1 Help http://resources.arcgis.com/en/help/main/10.1/

## Slide 23: Acknowledgements
Dr. Patrick Kennelly - Professor of Geography, Penn State University
Penn State Online Geospatial Program Instructors
David Bumbaugh – Reservoir Engineer, BP
Jacob Maggard – Geospatial Capabilities Team Lead, BP

## Slide 24: Questions? Comments?