## Slide 1: DEM Resolution Effects on Visibility
By: Kimberly Quirk

## Slide 2: Outline
Background
  What is Viewshed Analysis
  Why Does Resolution Matter
  The Challenge of Defining Terrain Groupings
Study Requirements
  Objectives
  Optimal Study Environment
  Study Parameters
  Workflow
Viewshed Analysis Pilot Results
  Viewshed Pilot Results
  Resolution Change Pilot Results

## Slide 3: What is Viewshed Analysis?
Typically shows two results: visible or not visible (Miller, 2011)
Usually use Bare-Earth DEMS (Miller, 2011)
Unlike many viewshed analysis methodologies, this study does not look for the ideal placement for Observee (highest place with the best view)
This analysis uses the terrain based on point location instead of ideal locations

## Slide 4
1m Resolution
90m Resolution
10m Resolution
30m Resolution
Why Does Resolution Matter?
1:3,000
Individual cell (pixel) size shrinks as resolution improves
Viewshed Analysis determines visibility at the cell level

## Slide 5: The Challenge of Defining Terrain Groupings
Hammond, 1954. Reproduced here for educational purposes only.
Mountains, plains, and hills fit into several groups.

## Slide 6: Additional Terrain Grouping Challenges
MacMillan and Shary, 2008. Reproduced here for educational purposes only. Dikau et. al. introduce elevation to further break down these classes.

## Slide 7: Objective
To understand the effects of a DEM’s resolution on viewshed analysis:
  How will visibility change as a DEM’s resolution changes?
    Ex: Will higher resolutions reveal different pockets of visibility / invisibility than courser data?
  Will patterns of visibility / invisibility be consistent across terrain types?
    Ex: Will a higher resolution DEM change visibility, regardless of if the terrain is mountainous or flat?

## Slide 8: Optimal Study Items
Test several resolutions across a broad spectrum
  Use the 1m DEM to determine study areas for all resolutions
Test several terrains to check for patterns
  Test several regions within the United States to confirm consistency and best capture the various characteristics of terrain types
USGS National Map: Areas with 1m DEMs: https://viewer.nationalmap.gov/advanced-viewer/

## Slide 9: Viewshed Parameters
The Viewshed:
  360 degrees per point
    5km radius
  4 Points
    Do not overlap
  30km X 30km Study Area

## Slide 10: Stratified Sampling
Areas will be grouped into different terrain types
Must have continuous 1m data for a 30 km X 30 km box
  Areas may look continuous at this scale, but may still have holes
4 Points are evenly distributed in sample area to prevent overlaps
USGS 1m DEM Index: https://www.usgs.gov/core-science-systems/ngp/3dep/3dep-product-metadata

## Slide 11
West Colorado Study Area

## Slide 12
Collect DEMs: USGS and CGIAR-CSI
Check for Quality
Preprocess Data
Run the Viewshed Tool
Create Visibility Viewsheds
Analyze the Data and Collect Results
1m, 10m, 30m, and 90m (STRM) DEMs
Use ArcPro to visually scan the area
Create a hillshade to show the quality of the DEM
If Needed: convert from IMG to TIF and Mosaic tiles
Clip to study area square and project to appropriate UTM
Use two observee heights: .5m and 1.71m
Workflow
Insert four-point feature class that will be the observee points

## Slide 13
1m Standing
1m Laying

## Slide 14
1m Standing
30m Standing
90m Standing
10m Standing
Pilot Viewshed Analysis

## Slide 15: Pilot Viewshed Analysis
Viewshed Results
Viewshed Resolution Changes

## Slide 16
1m Results
Pt 4
Pt 3
Pt 2
Pt 1

## Slide 17
10m Results
Pt 4
Pt 3
Pt 2
Pt 1

## Slide 18
30m Results
Pt 4
Pt 3
Pt 2
Pt 1

## Slide 19
90m Results
Pt 4
Pt 3
Pt 2
Pt 1

## Slide 20
90m
30m
10m
1m
The Changes
*Blue indicates areas captured on all resolution

## Slide 21
90m
30m
10m
1m
Point 1 Change
*Blue indicates areas captured on all resolution

## Slide 22
90m
30m
10m
1m
Point 2 Change
*Blue indicates areas captured on all resolution

## Slide 23
90m
30m
10m
1m
Point 3 Change
*Blue indicates areas captured on all resolution

## Slide 24
90m
30m
10m
1m
Point 4 Change
*Blue indicates areas captured on all resolution

## Slide 25
Present at Mountain Cartography Workshop - ICA
April
Complete Slides and Prep to Brief
May
Submit Final Report
March
Final determination of terrain types to be used, sample locations, and number of samples
Download DEM Data and perform visual checks and hillshade DEMs
Prepare DEMs for the tool.
Create Study’s rectangle
Run DEMs through the tool
Create the Individual Viewsheds
Analyze Results
January
Late January
February
February
December
January
Project Timeline

## Slide 26
Hammond, Edwin H. (1954). Small-Scale Continental Landform Maps. Annals of the
Association of American Geographers, 44(1), 3-42. https://www.jstor.org/stable/2561113
MacMillan, R. A. and Shary, P.A. (2008). Chapter 9 Landforms and Landform Elements
in Geomorphometry. Developments in Soil Science, 33, 227-254. https://doi.org/10.1016/S0166-2481(08)00009-3
Miller, Matthew L. (2011). Analysis of Viewshed Accuracy with Variable Resolution
LiDAR Digital Surface Models, and Photogrammetrically-Derived Digital Elevation Models. Virginia Polytechnic Institute and State University. https://pdfs.semanticscholar.org/d6c8/67904dfff3a50b3e709640fee0e052f766b5.pdf
Thelin, Gail P. and Pike, Richard J. (1991). Landforms of the Conterminous United
States—A Digital Shaded-Relief Portrayal. U.S. Department of the Interior U.S. Geological Survey. https://pubs.usgs.gov/imap/i2206/i2206_pamphlet.pdf
Thompson, James, Bell, Jay, and Butler, Charles (2001). Digital elevation model
resolution: effects on terrain attribute calculation and quantitative soil-landscape modeling. Geoderma, 100(1-2), 67-89. DOI: 10.1016/S0016-7061(00)00081-1
References