## Slide 1: Real Time Spray monitoring system
For Use in Industrial Vegetation Management
Joseph Wilde
The Pennsylvania State University

## Slide 2: Presentation Overview
Goals and Objectives
Project Background
System Requirements
System Components
Cost Analysis
Managerial Benefits
Additional Uses / Capabilities

## Slide 3: Goals and Objectives
Develop real time spray monitoring system
  Build / design required hardware interfaces
  Design a geospatial database to store all transmitted data
  Develop a data access webpage to query reports and maps from the database

## Slide 4: Project Background
Tracking and proving herbicide application activity on a large property is difficult
GPS can be used as means to prove services rendered in an area of dispute
Cellular data transfer allows for minimal operator interaction and training

## Slide 5: System Requirements
Functional Requirements
  Provide Active Vehicle Location (AVL) service
  Create a system that functions in all service areas
  Monitor application hardware in real time
  Maintain historical application records
  Provide activity reporting capabilities
  Develop data access webpage to spatial data
Business Requirements
  System cost should not inhibit use
  Seamless integration into work environment
    No additional burden on field crews

## Slide 6: System Components
Cellular Modem
Application Hardware
Spatial Database
Packet Handling Service
Data Access Front End

## Slide 7: System Components Cellular Modem
CalAmp LMU-4100 Series
  GPS Enabled
  Cellular data transfer
  Easily Programmable
  Digital I/O Interface

## Slide 8: System Components Cellular Modem - Modem Firmware
Sleep / wake logic for power conservation
Capture digital signals from hardware
  Ignition
  Spray state
  Flow rate
  Application type
    As determined through the custom wiring harness installed in each piece of equipment
Transmit system state on predetermined events
  Time or transition based events

## Slide 9: System Components Application Hardware
Raven Industries Flow Meter
Hand spray gun with custom wiring harness and waist battery pack

## Slide 10: System Components Spatial Database
Data stored in PostgreSQL relational database
PostGIS spatial extensions provide GIS capabilities
Debian based server for speed and reliability

## Slide 11: System Components Spatial Database - Database Schema
Schema rendered through OpenOffice.org-Base

## Slide 12: System Components Packet Handling Service
Listens for incoming modem transmissions
Parses binary data into useable format
Checks for transmission errors
Inserts validated data into database
Implemented in Python

## Slide 13: System Components Data Access Webpage
Secure web-based portal
Real time system information
  Application rate, GPS location, vehicle speed, etc
Full historic query capability
  By date, vehicle, application type, etc.

## Slide 14: System Diagram

## Slide 15: Internal Costs One Time Development Investment
Internal costs based on hourly rate of $25/hr
Note that these costs refer to system development and are incurred one time. Individual setup costs are discussed in External Costs below.
Item | Cost
Modem Firmware | $500.00
Wiring Harness | $750.00
Database Design | $6,500.00
Packet Handling Service | $1,500.00
Data Access Front End | $2,750.00
Total: | $12,000.00

## Slide 16: External Costs Reoccuring Hardware Investment
Modem cost is incurred once
Data handling fee is a flat rate per month regardless of modem use
Data usage varies on frequency and amount of information being sent
Item | Per-Unit Cost
CalAmp LMU-4100 | $331.00
Data Handling | $4.00 / month
Data Usage | $2.00 / megabyte

## Slide 17: Managerial Benefits
Equipment Inventory
Real Time Monitoring
Job Progress Monitoring
Progress Report Capabilities
Automatic Data Deliverables

## Slide 18: Managerial Benefits Equipment Inventory
Up to the minute AVL information
Efficient fleet mobilization planning
No manual input required to maintain vehicle location database

## Slide 19: Managerial Benefits Real Time Spray Monitoring

## Slide 20: Managerial Benefits Job Progress Monitoring
Overall Site progress
Application details
Configurable zoom levels provide access to variable levels of job progress information

## Slide 21: Managerial Benefits Progress Report Capabilities
Visual estimates of site completion
Graphs and charts depicting sites worked
Work completed summarized by:
  Operator
  Service Area
  Date
  Etc…

## Slide 22: Managerial Benefits Automatic Data Deliverables
Simple data exports on web front end
Supports a variety of common data formats
  ESRI Shapefiles
  Google KML files
  Garmin GPI files for NUVI navigation

## Slide 23: Future Markets
Basic fleet tracking
Department of Transportation / railroad right of way management
Infrastructure mapping
  Using toggle switches to mark assets

## Slide 24: Additional Capabilities
Accelerometer-based collision reporting systems
  Automatic alerts for accidents
Integrated ambient weather sensors
  Dictate whether conditions are right for spraying
Pressure / tank volume sensors
  Provide audio/visual queues to operators

## Slide 25: Resources
DeAngelo Brothers, Inc
  Project sponsored in full by Dbi for use in the Industrial Vegetation Management division.
Applocation Systems, Inc
  Calamp distributer. Provided initial technical support for modem communications.

## Slide 26: End
Questions / Comments?